## Slide 1: INTRODUCTION TO ELECTROCHEMICAL BIOSENSORS
Modern and future approaches to medical diagnostics
James F. Rusling
Depts. of Chemistry, Univ. CT
Dept. of Surgery & Neag Cancer Center, Uconn Health
School of Chemistry, NUI Galway, Ireland

## Slide 2: Sensors – all around us Foucault’s Pendulum (1851) (Palazzo della Ragione)
Earth's rotation causes the trajectory of the pendulum to change over time, monitored by a position sensor

## Slide 3: Medical Diagnostics
Doctors increasingly rely on testing
Needs: rapid, cheap, and “low tech”
Done by technicians or patients
Some needs for in-vivo operation, with feedback

## Slide 4
electrode
substrate
product
Enzyme
(label)
Apply voltage
Measure current prop.
to concentration of substrate
Principle of Electrochemical Biosensors
• Fast
• low cost
• high sensitivity
• possible to miniaturize

## Slide 5
E, V
time
E-t waveform
potentiostat
Electrochemical cell
counter
working electrode
N2
inlet
Protein film
Figure1
reference
insulator
electrode
material
Equipment for developing electrochemical biosensors
Cyclic
voltammetry

## Slide 6
RDVs of myoglobin-lipid film (a) on PG electrode with and without 3.9 mM ferredoxin (Fd) in pH 7 buffer; (b) Influence of ferredoxin concentration on Icat showing non-linear regression fit onto Michaelis-Menten model (solid line) and a linear fit to the simple EC' catalytic model (dashed line).
Example: Mb + Fd  Mb(Fd)  Mb + reduced Fd
kcat = 102 s-1 KM = 112 ,
kcat/KM = 9.1 x 104 M-1 s-1

## Slide 7
Catalytic enzyme electrochemistry
a basis for glucose biosensor - glucose oxidase
oxidation
Fc mediator
Fc + glucose
+ enzyme
I = f [glucose]
Mediator shuttles
Electrons between
Enzyme and electrode

## Slide 8
• Most sensors use enzyme called glucose oxidase (GO)
• Most sensors are constructed on electrodes, and use a
mediator to carry electrons from enzyme to GO
Fc = mediator, ferrocene, an iron complex
These reactions occur in the sensor:
Fc
Fc+ + e- (measured)
GOR + 2 Fc + --> GOox + 2 Fc
GOox + glucose --> GOR + gluconolactone
Reach and Wilson, Anal. Chem. 64, 381A (1992)
G. Ramsay, Commercial Biosensors, J. Wiley, 1998.

## Slide 9
Commercial Glucose Sensors
Biggest biosensor success story!
Diabetic patients monitor blood glucose at home
First made by Medisense (early 1990s), now 5 or more commercial test systems
Rapid analysis from single drop of blood
Enzyme-electrochemical device on a slide

## Slide 10
Glucose biosensor test strips (~$0.50-1.00 ea.)
Dry coating of GO + Fc
Patient Autopipettes drop of blood
onto slide; inserted into meter
Output:
Amperometry
Constant E, more sensitive than CV
I
t
Patient reads glucose
level on meter
e’s
electrodes

## Slide 11: Research on glucose sensors
Non-invasive biosensors - skin, saliva
Implantable glucose sensors to accompany artificial pancreas - feedback control of insulin supply
Typical use 3-4 weeks for implantable sensors in humans;
Failure involves fouling, inflammation
In vivo calibration? Auto-calibration?

## Slide 12: Other biosensors
Cholesterol - based on cholesterol oxidase
Antigen-antibody sensors - toxic substances, pathogenic bacteria, proteins
Small molecules and ions in living things: H+, K+, Na+, NH3, CO2, H2O2 (Abbott)
DNA genomic arrays and DNA damage
Micro or nanoarrays, optical abs. or fluorescence (proteins, small molecules)

## Slide 13
PSS layer
SPAN layer
Enzyme
layer
Detection of hydrogen peroxide
Conductive polymers efficiently wire
peroxidase enzymes to graphite
Xin Yu, G. A. Sotzing, F. Papadimitrakopoulos, J. F. Rusling, Highly Efficient Wiring of Enzymes to Electrodes by Ultrathin Conductive Polyion Underlayers: Enhanced Catalytic Response to Hydrogen Peroxide, Anal. Chem., 2003, 75, 4565-4571.
e’s
(sulfonated polyaniline,
Conductive polyion)

## Slide 14
Horseradish Peroxidase (HRP)
100nm
50nm
Tapping mode atomic force microscopy (AFM) image of HRP film

## Slide 16
Catalytic reduction of H2O2 by peroxidase films
Catalytic cycles increase current
FeIII/FeII
reduction

## Slide 17
3. Rotating electrode amperometry at 0 V
HRP, 50 nmol H2O2 additions
span
No span
reduction

## Slide 18
Rotating electrode amperometry at 0 V
Sensitivity much higher with conductive polymer (SPAN);
Electrically wires all the protein to electrode
Span/HRP
Span/Mb

## Slide 19
• detection by fluorescence, amperometry, electrochemiluminescence
• non-specific binding must be minimized
• commercial bead-based assays, expensive hardware
Nanoparticle Multilabel Strategies – high sensitivity

## Slide 20
Single-Walled Carbon Nanotube
Forests: Antigen-Antibody Sensing
SPAN or
Nafion
Chattopadhyay, Galeska, Papadimitrakopoulos, J. Am. Chem. Soc. 2001, 123, 9451.
End COOH groups allow chemical attachment to proteins (antibodies)
High conductivity to conduct signal (e’s) from enzyme label to meas. circuit
~1.4 nm diameter, high conductivity

## Slide 21
SWNT forests
bioconjugation

## Slide 22
Direct voltammetry of redox enzymes on SWNT forests - vectorial electron transfer
Direct cyclic voltammetry at
300 mV s-1 in pH 5.5 buffer
(b) Direct amperometry adding
H2O2 to HRP-SWNT; LOD 40 nM
not improved by mediator-->all HRP
is electrically wired
X. Yu, D. Chattopadhyay, I. Galeska, F. Papadimitrakopoulos, and J. F. Rusling, “Peroxidase activity of enzymes bound to the ends of single-wall carbon nanotubeforest electrodes”, Electrochem. Commun., 2003, 5, 408-411.

## Slide 23
AFM of SWNT forest with and without anti-HSA attached
SWNT forest on Si wafer
SWNT forest with anti-human serum
albumin (HSA) attached by amide links

## Slide 24
Enzyme Label Detection Chemistry:
use H2O2 and hydroquinone (HQ)
enzyme
A double catalytic process

## Slide 25
Cancer Biomarker Proteins: Prostate Specific Antigen
PSA - Single chain glycoprotein , MW 33 kDa
Sensitive, specific biomarker for detection of prostate cancer up to 5 years before clinical signs of disease
Detection of PSA in serum: clinical method for detection of prostate cancer
Led to less invasive treatment protocols, avoid surgery
Adapted From Brookhaven Protein Databank
With Drs. Silvio Gutkind and V. Patel, NIH

## Slide 26
Nanotube Strategies for PSA detection
~170 labels
per PSA

## Slide 27
Arrays can detect many biomolecules at once
multi-electrode sensor arrays
Sensing electrodes
electrical
contacts
An optical-
electrochemical
array
Polymer gives off light when electro-oxidized with proper co-reactant, e.g. DNA
Ink-jet
printing
Processed gold CDs

## Slide 28
Microfluidic capture chamber and detector are machined Polymethyl-methacrylate (PMMA) + soft PDMS channel + 8 sensor array
Kanichi Ltd., UK
Inkjet printed
4 nm AuNPs
Detector assembly
Molded
32 sensor array: wet etched gold CD with
insulation and nanowells
printed with computer ink,
and heat-transferred onto the PG chip

## Slide 29
Electrical contacts
electrodes
8-electrode PDMS fluidic array;
AuNP layer deposited on electrodes
Bhaskara V. Chikkaveeraiah, Vigneshwaran Mani, Vyomesh Patel, J. Silvio Gutkind, and James F. Rusling, Microfluidic electrochemical immunoarray for ultrasensitive detection of two cancer biomarker proteins in serum, Biosensors & Bioelectron. 2011, 26, 4477– 4483.

## Slide 30
Microfluidic protein assay system

## Slide 31
+
Sensor surface captures bead
+ protein for detection; sensor never
sees sample matrix
Label = HRP enzyme;
Activated by H2O2
Proteins in
sample
Multilabel Magnetic
bead-Ab2
Protein captured by
bead, magnetically
separated
Protein analyte capture with magnetic beads
greatly lowers non-specific binding

## Slide 32
Multiplexed Detection of Oral Cancer Biomarker Proteins:
IL-6, IL-8, VEGF, and VEGF-C
one sensor
protein capture on heavily
labeled particles

## Slide 33
Cancer Biomarker Proteins in Diluted Serum

## Slide 34: Biosensors
Future of medical diagnostics; use by patients or in doctors offices and clinics
Applications include cancer biomarkers, DNA, peroxide, etc.
Method of choice for blood glucose in diabetics
Rapid diagnostics may lead to more timely and effective treatment; need automation
Nanostructured electrodes and nanoparticle labels lead to high sensitivity